## Slide 1: ROBOTIC ARM SIMULATION
Presented By Mohammad Rohaan 22I-2327

## Slide 2: DH TABLE
JOINTS | LINK LENGTH | ALPHA | D | THETA
1 | A1 | -90 | D1 | THETA1
2 | A2 | 0 | 0 | THETA2
3 | A3 | 0 | 0 | THETA3
4 | 0 | 90 | D4 | THETA4

## Slide 3: TASKS OF ASSIGNMENT 01 02 03 04
FORWARD KINEMATICS
TRANSFORMATION MATRIX
INVERSE KINEMATICS
ARM SIMULATION

## Slide 4: TRANSFORMATION MATRIX
A transformation matrix is a 4x4 matrix used in robotics to represent both the position and orientation of a link in 3D space relative to another link. It combines rotation and translation, allowing precise calculation of each link's location, enabling the robotic arm's movements to be modeled and controlled accurately.

## Slide 5: TRANSFORMATION MATRIX 01
CODE TO FIND TRANSFORMATION MATRIX

## Slide 6
prompt = {'Enter theta1 (degrees):', 'Enter theta2 (degrees):', 'Enter theta3 (degrees):', 'Enter theta4 (degrees):'};
theta1 = deg2rad(theta1);
theta2 = deg2rad(theta2);
theta3 = deg2rad(theta3);
theta4 = deg2rad(theta4);
pose = app.forwardKinematics(theta1, theta2, theta3, theta4);
endEffectorPos = pose(1:3, 4);
disp(endEffectorPos);
var = sprintf('[%.1f %.1f %.1f %.1f\n %.1f %.1f %.1f %.1f\n %.1f %.1f %.1f %.1f\n %.1f %.1f %.1f %.1f]', ...
pose(1,1), pose(1,2), pose(1,3), pose(1,4), ...
pose(2,1), pose(2,2), pose(2,3), pose(2,4), ...
pose(3,1), pose(3,2), pose(3,3), pose(3,4), ...
pose(4,1), pose(4,2), pose(4,3), pose(4,4));

## Slide 7
if theta(i) < qmin || theta(i) > qmax
sprintf('Joint %d exceeds its limits! Valid range: [%.1f, %.1f]’)
figure('Name', 'SUMO_ROBO', 'NumberTitle', 'off', 'WindowState', 'maximized');
show(puma560, theta, 'Frames', 'off’);
app.TextArea.Value = {output_String};
app.TextArea.Visible = 'on';
pause(5);
app.TextArea.Visible = 'off';
puma560 = loadrobot('puma560', 'DataFormat', 'row', 'Gravity', [0 0 -9.81]);

## Slide 8: FORWARD KINEMATICS 02
CODE TO FIND FORWARD KINEMATICS

## Slide 9
prompt = {'Enter theta1 (degrees):', 'Enter theta2 (degrees):', 'Enter theta3 (degrees):', 'Enter theta4 (degrees):'};
theta1 = deg2rad(theta1);
theta2 = deg2rad(theta2);
theta3 = deg2rad(theta3);
theta4 = deg2rad(theta4);
JN = [theta1, theta2, theta3, theta4, 0, 0];
for i = 1:length(JN)
qmin = JN(i, 1);
if JN(i) < qmin
sprintf('Joint %d exceeds its limits!’);
return;
end

## Slide 10
EN = 'link4’;
position = transl(EN);
if app.isSingular(JN)
sprintf(‘LOST ONE ANGLE', position(1), position(2), position(3));
end
output_String = sprintf('\n\n End Effector Position:\n\nX = %.2f\nY = %.2f\nZ = %.2f', position(1), position(2), position(3));
app.TextArea.Value = {output_String};
app.TextArea.Visible = 'on';
app.TextArea.Visible = 'off';
figure('Name', 'SOMO', 'NumberTitle', 'off', 'WindowState', 'maximized');
show(p560, JN);

## Slide 11: INVERSE KINEMATICS 03
CODE TO FIND INVERSE KINEMATICS

## Slide 12
prompt = {'Enter X position:', 'Enter Y position:', 'Enter Z position:’};
r = sqrt(x^2 + y^2);
if r < 0.5 || r > 1
sprint('Position is outside the radial limits ');
return;
elseif theta < -90 || theta > 90
sprint('Position is outside the angular limits ');
return;
elseif z < 0
sprint('Z-position must be non-negative.', 'Workspace Error');
return;
end

## Slide 13
JN = ik('link6’, EN, weights, zeros(1, 6));
output_String = sprintf(rad2deg(jointAngles(1)), rad2deg(jointAngles(2)), rad2deg(jointAngles(3)), rad2deg(jointAngles(4)), rad2deg(jointAngles(5)), rad2deg(jointAngles(6)));
app.TextArea.Visible = 'on';
pause(5);
app.TextArea.Visible = 'off';
figure('Name', ‘SUMO_ROBO', 'NumberTitle', 'off', 'WindowState', 'maximized');
show(p560, jointAngles);

## Slide 14: SIMULAION 04
CODE FOR SIMULAION

## Slide 15
dh_table = {
'1', '0', '0.2', '0.5', '-90';
'2', '0', '0', '0.5', '0';
'3', '0', '0', '0.5', '0';
'4', '0', '0.1', '0', '-90';
'5', '0', '0', '0', '90';
'6', '0', '0', '0', '0'
};
dh = uifigure('Name', 'DH Table', 'NumberTitle', 'off');
dh.WindowState = 'maximized';

## Slide 16
T0 = eye(4);
T1 = transl(1, 2, 3) * rpy2tr(0.6, 0.8, 1.4);
figure;
trplot(T0);
hold on;
trplot(T1);
T_current = transl(S(idx, :)) * rpy2tr(0.6, 0.8, 1.4);
trplot(T_current);

## Slide 17: PRODUCT OVERVIEW
EARTH
Earth is the only planet that harbors life
VENUS
Venus is the second planet from the Sun
SATURN
Saturn is composed of hydrogen and helium
JUPITER
Jupiter is the biggest planet of them all
MERCURY
Mercury is the closest planet to the Sun
NEPTUNE
Neptune is the farthest planet from the Sun